I Material

1.1 Case

1.2 PCB

1.3 Indicators and controls on front panel

1.4 Connectors on rear panel

II Use of TH 02 RD

1.1 Installation

1.2 Adjustments

III Technical specifications

1.1 Technical parameters

1.2 Fig.1 - block diagram

IV Warranty

V  REMOTE CONNECTOR

I Material

1.1 Case

* 19", 1U format

* chassis: pasivated steel CD 5B, surface highly conductive

* NC controlled production

* excellent electromagnetic compatibility

* front panel is made from dural with plastic surface

* standard IEC power input

1.2 PCB

* 2 layer PCB

* minimalization of crosstalk by original method of virtual impedance

* ringing detector (RD) on PCB

* power transformer, indicators and connectors on board

1.3 Indicators and controls on front panel

1* Power check - LED lits, when power is ON

* Ring - red LED lits, when line is ringing, in the same time RD output on rear panel is activated

* Line ON - lits, when line is ON by TH 02

* Control ON/OFF - switch for activating of telephone line. In upper position, line is activated (ON).

* Crosstalk - pot for adjustment of minimal crosstalk between outcoming and incoming signal. Nominal position is aprox. center

* Bandwidth - pot for adjustment of bandwidth of incoming signal. Alows to adjust bandwidth from cca 2 kHz to 3.5 kHz, it depends   on quality of line (bad line - adjust 2 kHz (left), good line -adjust 3.5 kHz (right))

* Return - pot for adjustment of output level from TH 02

* Send - pot for adjustment of output level from TH 02 to telephone line. Recomendation: send to line only minimum          sufficient level. Crosstalk will be better.

1.4 Connectors on rear panel

* standard IEC connector for line input

* standard IEC connector for handset

* standard XLR connectors for line in and out (balanced)

* DB 15 male connector for remote control and RD output

* grounding screw for connection with another equipement

II Use of TH 02 RD

1.1 Instalation

* install TH 02 to dry place, avoid direct sunlight and heat

* use only correct power supply

* connect mixing desk output (aux output) to XLR balanced input

* connect mixing desk input (input of fader) to XLR balanced output

* if you have non - balanced input (for example cinch) don´t short second output pin of XLR to ground !!

* you can use remote control via remote connector on rear panel

* you can use RD output via remote connector on rear panel

* connect telephone line to line input, and handset to phone output

1.2 Adjustment

* make connection with somebody by telephone

* switch TH 02 to line ON

* ask other side for speaking

* adjust optimal output level (for your mix) of TH 02 by RETURN     pot

* ask other side for silence and hearing

* by SEND pot find optimal output level to phone line (on the output of   mix should be nominal level of speech signal)

* now hear output of TH 02, (on input is speech signal) and adjust   minimum crosstalk by CROSSTALK of TH 02 (minimal speech signal on XLR output of TH 02)

* finally adjust BANDWIDTH of TH 02 in dependence of quality of     line

* hang up phone line

III Technical specifications

1.1 Technical parameters

sending section:

frequency range:					330-3.3 kHz (-3dB)

input sensitivity:					1.55 V (adjustable +/-6dB)

inputs/outputs:		   				electronically balanced

input impedance:					10 kohm

sending level:						-10 dBu

return section

nominal output level:					1.55 V (adjustable +/-6dB)

output impedance:					100 ohm

maximal output voltage:					8 V

frequency range:					330-3.3 kHz (-3dB)

receiving level:					-10 dBu

crosstalk send/receive:					25 dB min

supply voltage:					220V

fuse:							32 mA

working temperature range:				0 - 40 gr.Celsia

dimensions:						19", 1U

mass:						cca 4.4 kg

IV Warranty

* Phobos Audio gives to you 1 year warranty from purchase  excluding unauthorised manipulation.

Producer: Phobos Engineering s.r.o. Provoz: U družstva Život 4, Praha 4, 140 00, tel-fax: +4202 41412938

www.phobosaudio.cz

phobosaudio@email.cz